## Slide 1: Bilevel Optimization of Transmission and Distribution Systems

## Slide 2: Motivation
Motivation: currently distribution system(DS) is a passive component is the optimization problem, we want to incorporate DS information in the problem, optimize the DS results. Will compare the performance of the bilevel optimization approach with the traditional ISO’s approach

## Slide 3: Current ISO’s Approach
Objective function: min(generation bids + reserve bids + DS demand bids + DS DR bids)
Variables: generation, reserve, demand, DR
Philosophy: minimize the total operation cost by having all the cost terms in one objective function, the decision of the individual DS is out of the DS’s control

## Slide 4: Bilevel Optimization Approach
Upper level obj: min(generation&reserve bid + DS
DR cost – DS import revenue)
Upper level variables: generation, import & DR price
Lower level obj: min(DS demand bids + DS DR bids
DS DR revenue + DS import cost)
Lower level variables: load, import & DR quantity
Philosophy: leader(TS) decides DR and import price,
Follower(DS) decides import & DR quantity
Upper Level:
TS Unit Commitment
Lower Level:
DS Optimal Dispatch
DS DR
DS
import
DS DR,
import/export
price

## Slide 5: Results
Chart: Total System Cost：TS+DS
| Bilevel | Traditional | Traditional With Network
 | 6925 | 6738 | 6831
Chart: DS Cost
| Bilevel | Traditional | Traditional With Network
 | -3587 | -3440 | -3367
*DS cost for the traditional approach is posterior cost
with the LMP as the import and DR price.

## Slide 6: Results: environmental effects
 | Drup (MW) | Drdn (MW) | Reserve up (MW) | Reserve dn (MW) | DR price ($/MW)
Bilevel | 63 | 63 | 5 | 135 | 2.66
Traditional with Network | 102 | 63 | 5 | 96 | 3.52

## Slide 7: Results: 3 DS
Chart: DS Cost
| Bilevel | Traditional With Network
 | -3738 | -3266
Chart: Total System Cost：TS+DS
| Bilevel | Traditional With Network
 | 556 | 217

## Slide 8: Results: environmental effects
 | Drup (MW) | Drdn (MW) | Reserve up (MW) | Reserve dn (MW) | DR price ($/MW)
Bilevel | 68 | 68 | 5 | 130 | 1.5
Traditional with Network | 180 | 68 | 0 | 17 | 3.66